## Slide 1
Vibration-Based Condition Monitoring
System for Rotating Fans
Github:
https://github.com/Ayunoo/Condition-Monitoring-Project
Youtube video:
https://youtu.be/3-jeOoLR8ko
Name | Matric no
Adrien Pierre MALCOIFFE Wei YAGE | MEM241042 MEM241043

## Slide 2
Part 1：System Overview & Data Acquisition
Part 2：Data Transmission & Preprocessing
Part 3：Fault Simulation & Signal Analysis
Part 4：Feature Extraction & Intelligent Diagnosis
Part 5：Model Evaluation & Result Display

## Slide 3
Develop a simple and efficient condition monitoring system for rotating fans.
Collecting real-time vibration data during fan operation using MPU6050 sensors and Arduino Uno
Analyzing the data through signal processing and machine learning techniques
Detecting and classifying typical faults such as mechanical imbalance in real time.
Objectives

## Slide 4
I. Data collection:
（1）Sensor Selection: MPU6050 sensor
A three-ais accelerometer
（2）Control hardware: Arduino Uno
For the data acquisition
（3）Acquisition content: including vibration signals and acceleration along each axis
Part 1：System Overview & Data Acquisition
(1)
(2)
(3)
x
z
y

## Slide 5
(1) Data transmission: Raw data transmitted to the computer
(2) Data storage: Save the vibration signal
(3) Signal Analysis: Applying FFT to analyze frequency domain
(4) Fans faults detected after analyzing harmonics
Part 2：Data Transmission & Preprocessing

## Slide 6
Purposely adding a small piece of paper on the fan blade
This setup facilitates subsequent comparative analysis between normal and faulty states
At the end, we will be able to create an alert if unbalance occurs.
Failure simulation methodology:
Part 3：Fault Simulation & Signal Analysis

## Slide 7
normal condition
unbalanced condition
Part 3：Fault Simulation & Signal Analysis
In the Y-axis vibration signal, the amplitude of the 12.5 Hz peak increases by 76% in unbalanced condition.

## Slide 8
Software Identification and Diagnostics Module:
The signal processing and analysis part includes modules for signal receiving, storage, and data analysis.
A dedicated tool to extract various time-domain and frequency-domain features from the signals.
The system integrates a decision tree-based machine learning model to automatically classify and identify the fan's operating state.
Part 4：Feature Extraction & Intelligent Diagnosis

## Slide 9
It automatically calculates key indicators such as peak value and RMS for time-domain features, and kurtosis, waveform factor, etc. for dimensionless features.
These help quantify differences between normal and faulty states.
Part 4：Feature Extraction & Intelligent Diagnosis

## Slide 10
Real-time identification of 5 fan states: speed1/2/3, unbalance fault1/2
Decision tree-based classification trained on input features and outputing current fan condition
Displayable decision tree and visual diagnosis
Part 4：Feature Extraction & Intelligent Diagnosis

## Slide 11
The confusion matrix module shows the model’s performance in multi-class fault classification
The accuracy curve tracks training and validation accuracy over epochs
Part 5：Model Evaluation & Result Display

## Slide 12
Diagnosis process: visual, interpretable, traceable, and providing users with a clear and transparent intelligent fault diagnosis experience.
All states were successfully identified, demonstrating the system’s effective fault warning capability.
Part 5：Model Evaluation & Result Display

## Slide 13
(1) Turning it into a 24h/24h working system
(3) Detect other issues like misalignement
(3) Improve the overall design of the sensor
To go further…

## Slide 14
Thank you for listening